## Slide 1
UE
gNB
SR (Scheduling Request)
UL Grant (DCI 0_1)
PUSCH (Data)
UE requests grant
gNB allocates
UE transmits
STANDARD GRANT-BASED SCHEDULING vs GRANT-FREE SCHEDULING
UE
gNB
PUSCH (Data)
UE transmits
Pre-configured resources known
Listening on configured resources

## Slide 2
GRANT-FREE SCHEDULING ALGORITHM
UE
GNB
Before any transmission happens, both UE and gNB must have matching configurations
WHEN to transmit:
• periodicity = 4 slots (transmit every 4 slots)
• offset = 0 (starting from slot 0)
WHERE in frequency:
• rb_start = 0 (start at PRB 0)
• rb_size = 10 (use 10 PRBs)
WHERE in time (within slot):
• start_symbol = 2 (start at OFDM symbol 2)
• nr_of_symbols = 12 (use 12 symbols)
HOW to transmit:
• mcs = 9 (modulation and coding scheme)
• harq_process_id = 0 (dedicated HARQ process)

## Slide 3
UE Transmission Path
GF Occasion Detection
Every slot, the UE checks: "Is this a Grant-Free occasion?"
Formula: (absolute_slot - offset) % periodicity == 0
Where: absolute_slot = frame × slots_per_frame + slot
Calculation:
Slot 0: (0 - 0) % 4 = 0 ✓ GF occasion
Slot 1: (1 - 0) % 4 = 1 ✗ Not GF
Slot 2: (2 - 0) % 4 = 2 ✗ Not GF
Slot 3: (3 - 0) % 4 = 3 ✗ Not GF
Slot 4: (4 - 0) % 4 = 0 ✓ GF occasion

## Slide 4
UE Transmission Path
Check Pending Data
If it's a GF occasion, the UE checks: "Do I have data to send?"
RLC Buffers:
LCID 1 (SRB) → 0 bytes
LCID 4 (DRB) → 500 bytes
LCID 5 (DRB) → 200 bytes  Total: 700 bytes pending
LCID 6 (DRB) → 0 bytes
If total > 0 → Proceed to TX
If total = 0 → Skip this occasion (or send BSR only)

## Slide 5
UE Transmission Path
Build MAC PDU
The UE constructs a MAC PDU that fits exactly into the TBS:
BSR │ SDU #1 │ SDU #2 │ PADDING
(2 bytes) (variable) (variable) (fill rest)
BSR (Buffer Status Report):
- Header + Data(Tells gNB how much more data UE has).
SDU (Service Data Unit):
- Header + RLC PDU Data(Actual user data )

## Slide 6
UE Transmission Path
Configure PHY (PUSCH PDU)
The UE configures the PHY layer with all transmission parameters.
The UE configures the PHY layer with all transmission parameters:
  Identity
  Resource Allocation
  Modulation & Coding
  HARQ
  DMRS
  Payload

## Slide 7
UE Transmission Path
PHY Transmits PUSCH
The PHY layer performs the transmission.

## Slide 8
gNB Reception Path
PHY Decode
The gNB PHY receives and decodes the signal.
MAC Layer Hook
The gNB MAC checks if this is a Grant-Free transmission. Otherwise → Normal grant-based PUSCH. Continue with standard processing
GF Reception Processing (Problem!!!)
[NR_MAC] Invalid PDU in 814.3 for RNTI 988F! mac_subheader_len: 1, mac_len: 6, remaining pdu_len: 3
[NR_MAC] Invalid PDU in 865.13 for RNTI 988F! mac_subheader_len: 1, mac_len: 8, remaining pdu_len: 3

## Slide 9
gNB Reception Path
MAC PDU Parsing
If the GF Reception Processing works correctly the gNB extracts the contents from the MAC PDU.
HARQ Feedback
gNB Sends ACK/NACK (TODO)
UE Handles Feedback from the gNB (TODO)

## Slide 10
Problem, how to resolve it (maybe)
TBS (Transport Block Size) Mismatch
The gNB scheduled a grant with a certain TBS, but the UE transmitted with different parameters, because maybe the gNB does not still see the GF configuration
Grant-Free Collision
If Grant-Free is active and transmitting on resources that overlap with scheduled grants (GBS), it could corrupt the scheduled PUSCH reception.
Synchronization Issue (I don’t think is our case)
BSR/Buffer Size Issue
The UE is reporting more data than it actually has, leading to padded or incomplete transmissions.